## Slide 1: Introduction to communication systems
Sdr stem camp
Developed by: Spencer grady & hunter litke

## Slide 2: Communication system basics
A communication system conveys information from its source to a destination
Examples include
  Telephone
  TV
  Radio
  Satellite
Notes: -

## Slide 3: Communication System basics
A communication system has the following components at its simplest form
Notes: - Instructor should walk through each component and give a brief description of what each one does. There are slides following this one that instructors can use to reference

## Slide 4: Input Transducer
The input transducer converts the original message that is produced by a source to a signal in an acceptable form for the communication system.
Example:
  Voice MICROPHONE Voltage
Notes: A perfect example of an input transducer is a microphone.
A microphone converts the users voice, which are sound waves, into an appropriate signal form for transportation.

## Slide 5: Transmitter
A transmitter couples the message to the channel and is responsible for sending the data. They also modulate and/or amplify the signal to send the message.
Example:
  TV and Radio stations broadcasting their content

## Slide 6: Channel
A channel is the physical medium that the message is transmitted over.
No channel is perfect, so signals become distorted, pick-up noise, or interference.
Example:
  Air, wires, EM waves

## Slide 7: Receiver
The receiver receives/extracts the message/signal.
The receiver can amplify and/or demodulate the signal.
Example:
  TV, radio

## Slide 8: Output Transducer
The output transducer converts the signal the proper form for the system.
Example:
  Loudspeakers

## Slide 9: Limitations
Bandwidth is one of the key limitation of communication systems.
Bandwidth: Bandwidth is the range of frequencies related to a system.
Examples of system with different bandwidths:
  AM Radio, FM Radio, TV, cellular networks, satellite, air traffic control

## Slide 10: Limitations
Noise is the other key limitation of a communication system. There is internal and external noise.
Think of noise in communication systems the same way you would if you were trying to hear what someone is saying at a loud stadium.
Internal Noise is generated by components within the system.
External noise is generated by components outside of the system.

## Slide 11: Bandwidths